PAGE 1 OF 4: SINK DETERGENT

APPLAUD PLC PTY. LTD.

SAFETY DATA SHEET

NON-Hazardous Substance, NON-Dangerous Goods

ACTIVE SOLUTIONS – SINK DETERGENT

1. Identification of the material and supplier

Names

Product name		: SINK DETERGENT

Supplier		: APPLAUD PLC PTY LTD

8 STEPHENSON ROAD

SEAFORD VIC. 3198

TELEPHONE:  (03) 9775 0443

FAX:(03)  9775 0312

MOBILE: 0411 353 793

Emergency telephone	: Normal Office Hours: Monday to Friday 8.30 to 5.00 pm (EST), (03) 9775 0443

number			  Poisons Information Centres: 13 11 26 (Australia wide)

Emergency Services: 000 or Refer to Local Telephone Directory

Uses

Material uses		: Liquid detergent

Date of issue		: 17-February-2020

2. Hazards identification

Based on available information, this material is not classified as hazardous according to criteria of Safe Work Australia.

Signal Word		Not Applicable.

Hazard Classifications	Serious Eye Damage/Irritation – Category 2B

Hazard Statements	Not allocated.

Precautionary Statements

Prevention		Not allocated.

Response		Not allocated.

Storage	Not allocated.

Disposal	Not allocated.

Poison Schedule: 	Not applicable.

DANGEROUS GOODS CLASSIFICATION

Not classified as Dangerous Goods by the criteria of the “Australian Code for the Transportation of Dangerous Goods by Road & Rail”.

3. Composition/information on ingredients

| 1-Propanaminium, 3-amino-N-(carboxymethyl)-N,N-dimethyl-, N-coco acyl derivatives, hydroxides, inner salts | 61789-40-0 | 1-10% |
| --- | --- | --- |
| Benzenesulfonic acid, dodecyl-, sodium salt | 25155-30-0 | 1-10% |
| Fatty acids, coco, compounds with diethanolamine | 61790-63-4 | 1-10% |
| Ingredients determined to be non-hazardous |  | Balance |

PAGE 2 OF 4: SINK DETERGENT

4. First –aid measures

First-aid measures

Eye contact		: Rinse with plenty of running water. Get medical attention if symptoms occur

Skin contact		: Flush contaminated skin with plenty of water. Obtain medical attention if symptoms occur

Inhalation		: Remove to fresh air. Obtain medical attention if symptoms occur.

Ingestion		: Do not induce vomiting. Rinse mouth; then drink one or two glasses of water.

Contact a doctor or a Poisons Information Centre (Phone: 13 11 26).

Notes to 		: No specific treatment. Treat symptomatically.

Physician

5. Fire-fighting measures

Extinguishing media	: Use an extinguishing agent suitable for the surrounding fire.

Fire/explosions hazards	: No specific hazard.

Special protective	: Fire fighters should wear appropriate protective equipment and self-contained breathing

Equipment for 		  apparatus (SCBA) with a full face-piece operated in positive pressure mode.

Fire fighters

Hazardous 		: These products are carbon oxides (CO, CO²).

Decomposition

Products

6. Accidental release measures

Personal Precautions	: Immediately contact emergency personnel. Keep unnecessary personnel away. Use suitable

protective equipment.

Environmental 		: Avoid dispersal of spilt material and runoff and contact with soil, waterways, drains and sewers.

Precautions

Methods for		: If emergency personnel are unavailable, contain spilt material. For small spills, add absorbent (soil Cleaning up	 	  may be used in the absence of other suitable materials), scoop up material and place in a

sealable, liquid- proof container for disposal. For large spills, dyke spilt material or otherwise

contain material to ensure runoff does not reach a waterway.

Place spilt material in an appropriate container for disposal.

Note: see section 8 for personal protective equipment and section 13 for waste disposal.

7. Handling and storage

Handling 		: Avoid contact with eyes, skin and clothing. Wash thoroughly after handling.

Storage			: Keep container tightly closed. Keep container in a cool, well-ventilated area.

Keep away from incompatibles, such as strong oxidizing material.

8. Exposure controls/personal protection

Occupational exposure	: No exposure standard allocated.

limits

Engineering measures	: None required. However, use of adequate ventilation is good industrial practice.

Hygiene measures	: Wash hands, forearms and face thoroughly after handling chemical products, before eating, smoking 		  and using the lavatory and at the end of the working period. Appropriate techniques should be

used to remove potentially contaminated clothing. Wash contaminated clothing before reusing.

Ensure that eyewash stations and safety showers are close to the workstation location.

Personal protection

Eyes			: Recommended: Safety glasses.

Hands			: Recommended: PVC gloves.

Respiratory		: A respirator is not needed under normal and intended conditions of product use.

Skin			: No special protective clothing is required.

PAGE 3 OF 4: SINK DETERGENT

9. Physical and chemical properties

Physical state		: Clear Viscous liquid

Colour			: Green

Odour			: Orange fragrance

Boiling point		: -

Melting Point		: -

Vapour pressure	: -

Specific gravity		: approx 1.0

Flash point		: n/a

Vapour density		: n/a

pH concentrate		: 7.0-8.5

pH 1%			: 7.0-8.0

Solubility		: Easily soluble in cold water, hot water.

10. Stability and reactivity

Stability			: The product is stable under normal ambient conditions of temperature and pressure.

Conditions to avoid	: None identified.

Materials to avoid	: Strong oxidizing agents.

Hazardous		: These products are carbon oxides (CO, CO2).

Decomposition

Products

Hazardous Reactions	: No hazardous reactions expected.

11. Toxicological information

Potential acute health effects

Inhalation		: No known significant effects or critical hazards.

Ingestion		: Exposure can cause nausea, headache and vomiting.

Skin contact		: No known significant effects or critical hazards.

Eye contact		: Slightly irritating to the eyes.

Potential chronic health effects

Carcinogenicity		: No known significant effects or critical hazards.

Mutagenicity		: No known significant effects or critical hazards.

Reproductive toxicity	: No known significant effects or critical hazards.

12. Ecological information

Ecotoxicity data		: n/a

Persistence/		: n/a

Degradability

Mobility			: n/a

Other adverse effects	: No known significant effects or critical hazards.

13. Disposal considerations

Methods of disposal	: Do not reuse product containers. The generation of waste should be avoided or minimised

wherever possible. Avoid dispersal of spilt material and runoff and contact with soil, waterways,  				  drains and sewers. Disposal of this product, solutions and all  by-products should at all times

comply with the requirements of environmental protection and waste disposal legislation

and any local authority requirements.

14. Transport information

| Regulation | UN Number | Proper shipping name | Class | Packing group | Additional information |
| --- | --- | --- | --- | --- | --- |
| ADG | - | Not regulated | - | - | - |

PAGE 4 OF 4: SINK DETERGENT

15. Regulatory information

Australian Inventory	: All substances are listed on AICS or exempt.

Status

AU Classification	: Not classified as hazardous according to the criteria of NOHSC.

Standard for the Uniform Scheduling of Drugs and Poisons

Not scheduled

Control of Scheduled Carcinogenic Substances

Ingredient name

No listed substance

16. Other information

Prepared by		: David Greasley

Date of previous issue	: March 2016

Change Made		: New GHS Format

The information contained herein is to the best of our knowledge correct and complete. It is meant to describe safety requirements of this product and no warranty, express or implied is made as to its fitness for a particular purpose or any other nature as to the product to which it refers.

If you are an employer it is your duty to tell your employees, and any others that may be affected, of any hazards described in this sheet and of any precautions that should be taken.